## Slide 1: TAWSS and OSI Fluent Calculation Guide
By: Asad Mirza
For: CV-PEUTICS

## Slide 2: Setting Up Fluent Export
Calculation Activities  Create  Solution Data Export
File Type: ASCII
Location: Node
Delimiter: Comma
Surface: Surface whose OSI/TAWSS you’re interested in
Quantities: Wall Shear Stress and XYZ Wall Shear Stress

## Slide 3: Exported Data

## Slide 4: Post-Processing: Setting Parameters
The MATLAB script titled “Fluent_Post_Processing_OSI_TAWSS.m” must be run to process the exported data.
It will ask you for the following:
  Simulation Start Time
  Simulation End Time
  Time Step Size
  Cycle Period
You will then be asked which results you wish to plot: TAWSS, OSI , or both.

## Slide 5: Post-Processing: TAWSS/OSI Plotting
Ex: +1 m/s Inlet
Ex: +/- 1 m/s Inlet

## Slide 6: Post-Processing: More Examples
Ex: S35/4 Waveform
Ex: Inlet Squared by 4 Waveform

## Slide 7: Future Improvements
Proper surface/element plotting rather than point cloud
Faster processing of many points
Reporting of Average +/- Standard Deviation for the exported surface
Creation of interactive GUI to simplify data processing.
Export GUI as exe to allow function outside of MATLAB