## Slide 1: Hemodynamic Fluent Calculation Guide
By: Asad Mirza
For: CV-PEUTICS

## Slide 2: Setting Up Fluent Export
Calculation Activities  Create  Solution Data Export
File Type: ASCII
Location: Node
Delimiter: Comma
Surface: Surface whose OSI/TAWSS you’re interested in
Quantities: Wall Shear Stress and XYZ Wall Shear Stress

## Slide 3: Exported Data

## Slide 4: Post-Processing: Setting Parameters
The MATLAB script titled “Fluent_Post_Processing.m” must be run to process the exported data.
It will ask you for the following:
  Simulation Start Time
  Simulation End Time
  Time Step Size
  Cycle Period
You will then be asked which results you wish to plot: TAWSS, OSI, RRT, or transWSS

## Slide 5: Post-Processing: TAWSS/OSI/RRT/transWSS
Measures average WSS on a surface over time.
Measures a fluid particle’s relative time spent in a particular location on a surface over time.
Measures average of the degree of forward/backward fluid movement on a surface over time.
Measures multidirectional WSS on a surface over time.

## Slide 6: Post-Processing: TAWSS/OSI Plotting
Ex: +1 m/s Inlet
Ex: +/- 1 m/s Inlet

## Slide 7: Post-Processing: RRT/transWSS
Ex: +1 m/s Inlet
Ex: +/- 1 m/s Inlet

## Slide 8: Post-Processing: More Examples (TAWSS/OSI)
Ex: S35/4 Waveform
Ex: Inlet Squared by 4 Waveform

## Slide 9: Post-Processing: More Examples (RRT/transWSS)
Ex: S35/4 Waveform
Ex: Inlet Squared by 4 Waveform

## Slide 10: Future Improvements
Proper surface/element plotting rather than point cloud
Faster processing of many points
Reporting of Average +/- Standard Deviation for the exported surface
Creation of interactive GUI to simplify data processing.
Export GUI as exe to allow function outside of MATLAB

## Slide 11: Comparing MATLAB TAWSS with Fluent Mean WSS
MATLAB
Fluent
Error Between Means = 1.305%